## Slide 1
TUTORIAL QUESTIONS
Embedded Processors, Caches and On-Chip Buses
Daniel Mueller-Gritschneder
Technical University of Munich
Department of Electrical and Computer Engineering
Chair of Real-Time Computer Systems
Real-Time and Embedded Systems @ SIT

## Slide 2: Questions on RISC-V Instruction Set Architecture

## Slide 3: Questions on RISC-V ISA?
Q1: Can you mix C-Code and assembly code in one project? What do you need to take care about?
Q2: what is the RISC-V instruction to add register a1 and a2 and store the result in a0?
Q3: What is the RISC-V instruction to subtract 4 from register a1 and save the result in register a2?
Q4: What alternative instruction can you use to multiply a value by 4 if you do not want to use the MUL instruction?
Q5: Your current PC value is 0x 00 AA 00 00; what is the Pc value after executing the instruction J 16?

## Slide 4: Answers on RISC-V ISA?
A1: Yes, but you need to make sure that the assembly code uses the ABI calling conventions, e.g., putting the return value in a0 etc.
A2: ADD a0,a1,a2
A3: ADDI a2,a1,-4 (Careful, there is no SUBI instruction)
A4: SLLI a1,a1,2
  Since the values are stored in binary (1’complement) a shift by 2 positions to the right is equal to a multiplication by 4.
  Example: 3 = 0b0011; (3 << 2) = (0b0011 << 2) = 0b1100 = 12 = 3 * 4
A5: PC = 0x00AA0000 + (offset <<1) = 0x00AA0000 + 16 << 1 = 0x 00AA0000 + 32 = 0x00AA0000 + 0x20 = 0x00AA0020;

## Slide 5: Problems on Writing RISC-V Assembly Code

## Slide 6: Questions on RISC-V Assembly
Q1: Translate the following C program to RISC V assembly:
int acc (int[4] x)
{
int z;
z= x[0] + x[1] + x[2] + x[3];
return z;
}

## Slide 7: Questions on RISC-V Assembly
int acc (int[4] x)
{
int z;
z= x[0] + x[1] + x[2] + x[3];
return z;
}
A1:
// a0: x, t0: z; t1: x[i]
acc:
LW t0,(a0) // z=x[0]
ADDI a0,a0,4
LW t1,(a0) // t1=x[1]
ADD t0,t0,t1 // z = z + x[1]
ADDI a0,a0,4
LW t1,(a0) // t1=x[2]
ADD t0,t0,t1 // z = z + x[2]
ADDI a0,a0,4
LW t1,(a0) // t1=x[3]
ADD t0,t0,t1 // z = z + x[3]
MV a0,t0 // z must be returned in a0
RET

## Slide 8: Problems on Embedded Processor RISC Architecture
Single-Cycle

## Slide 9: Questions on Single-cycle Processor 1
Q1: Put in the diagram below all bus values when the processor executes the instruction ADDI a1,a2,4
PC
Instruction Memory
IR
+4
NPC
Registers
A
B
M
U
x
M
U
x
Sign Extend
imm
ALU
ALU output
Data Memory
LMD
M
U
x
M
U
x
Branch
Taken?

## Slide 10: Questions on Single-cycle Processor 2
Q2: Put in the diagram below all bus values when the processor executes the instruction BNE a1,a2,-8 for the case the branch is not taken!
PC
Instruction Memory
IR
+4
NPC
Registers
A
B
M
U
x
M
U
x
Sign Extend
imm
ALU
ALU output
Data Memory
LMD
M
U
x
M
U
x
Branch
Taken?

## Slide 11: Answers on Single-cycle Processor 1
A1: ADDI a1,a2,4
PC
Instruction Memory
IR
+4
NPC
Registers
A
B
M
U
x
M
U
x
Sign Extend
imm
ALU
ALU output
Data Memory
LMD
M
U
x
M
U
x
Branch
Taken?
pc
MEM[pc]
pc+4
regs[a2]
regs[a2]+4
pc+4
regs[a1]
regs[a2]
4
a2
4
a1
regs[a2]+4
regs[a2]+4
pc+4

## Slide 12: Answers on Single-cycle Processor 2
A2: BNE a1,a2, -8 for the case the branch is not taken!
PC
Instruction Memory
IR
+4
NPC
Registers
A
B
M
U
x
M
U
x
Sign Extend
imm
ALU
ALU output
Data Memory
LMD
M
U
x
M
U
x
Branch
Taken?
pc
MEM[pc]
pc+4
pc-16
pc+4
-8<<1 = -16
pc
-16
pc+4
regs[a1]
regs[a2]
a1
a2
regs[a1]
regs[a2]
False meaning a1 == a2
pc

## Slide 13: Problems on Embedded Processor RISC Architecture
Pipelined

## Slide 14: Questions on Pipelined Execution
Q1: Taken the following assembly code of the function foo1. How many clock cycles does the execution take on a pipelined processor (standard 5 stages)
(a) without forward paths?
(b) with forward paths?
What is the CPI in both cases?
(c) Can the solution in (b) be improved by changing the program?
// a0: x, a1:b, t0: z; t1: x[i]
foo1:
LW t0,(a0) // z=x[0]
SLL t0,t0,a1 // z = z << b
ADDI a0,a0,4
LW t1,(a0) // t1=x[1]
ADDI a1,a1,1
SLL t1,t1,a1 // t1 = x[1] << (b+1)
ADD t0,t0,t1 // z = z + (x[1] << (b+1))
MV a0,t0 // z must be returned in a0
RET

## Slide 15: Answer on Pipelined Execution 1
A1 (a) without forward paths?
// a0: x, a1:b, t0: z; t1: x[i]
foo1:
LW t0,(a0) // z=x[0]
SLL t0,t0,a1 // z = z << b
ADDI a0,a0,4
LW t1,(a0) // t1=x[1]
ADDI a1,a1,1
SLL t1,t1,a1 // t1 = x[1] << (b+1)
ADD t0,t0,t1 // z = z + (x[1] << (b+1))
MV a0,t0 // z must be returned in a0
RET
1 clock cycle
Alu after load data hazard -> costs 2 clock cycles without forwarding
3 clock cycle
1 clock cycle
3 clock cycle
1 clock cycle
3 clock cycle
Alu after alu data hazard -> costs 2 clock cycles without forwarding
Alu after alu data hazard -> costs 2 clock cycles without forwarding
3 clock cycle
Alu after alu data hazard -> costs 2 clock cycles without forwarding
3 clock cycle
3 clock cycle
RET is a branch -> costs two clock cycles due to control hazard
# Instr = 9
# Clock cycles = 21
CPI = 21 / 9 = 2,33
Load-use hazard, need to align LW EX with ADDI WD

## Slide 16: Answer on Pipelined Execution 2
A1 (b) with forward paths?
// a0: x, a1:b, t0: z; t1: x[i]
foo1:
LW t0,(a0) // z=x[0]
SLL t0,t0,a1 // z = z << b
ADDI a0,a0,4
LW t1,(a0) // t1=x[1]
ADDI a1,a1,1
SLL t1,t1,a1 // t1 = x[1] << (b+1)
ADD t0,t0,t1 // z = z + (x[1] << (b+1))
MV a0,t0 // z must be returned in a0
RET
1 clock cycle
Alu after load data hazard -> costs 1 clock cycles with forwarding
2 clock cycle
1 clock cycle
1 clock cycle
1 clock cycle
1 clock cycle
Alu after alu data hazard -> no cost with forwarding
Alu after alu data hazard -> no cost with forwarding
1 clock cycle
Alu after alu data hazard -> no cost with forwarding
1 clock cycle
3 clock cycle
RET is a branch -> costs two clock cycles due to control hazard
# Instr = 9
# Clock cycles = 12
CPI = 12 / 9 = 1,33

## Slide 17: Answer on Pipelined Execution 3
A1 (c) with forward paths? Improvement?
// a0: x, a1:b, t0: z; t1: x[i]
foo1:
LW t0,(a0) // z=x[0]
ADDI a0,a0,4
SLL t0,t0,a1 // z = z << b
LW t1,(a0) // t1=x[1]
ADDI a1,a1,1
SLL t1,t1,a1 // t1 = x[1] << (b+1)
ADD t0,t0,t1 // z = z + (x[1] << (b+1))
MV a0,t0 // z must be returned in a0
RET
1 clock cycle
REMOVES Alu after load data hazard
1 clock cycle
1 clock cycle
1 clock cycle
1 clock cycle
1 clock cycle
Alu after alu data hazard -> no cost with forwarding
Alu after alu data hazard -> no cost with forwarding
1 clock cycle
Alu after alu data hazard -> no cost with forwarding
1 clock cycle
3 clock cycle
RET is a branch -> costs two clock cycles due to control hazard
# Instr = 9
# Clock cycles = 11
CPI = 11 / 9 = 1,2
Reorder these two statements

## Slide 18: Problems on Estimating Execution Time

## Slide 19: Question on Execution Time
Q1. Given the following system and application, what is the execution time estimate?
System:
fclock = 100 MHz CPI 1.5 for all instr.
Instruction fetch always take 1 cycle.
Stores always take 1 cycle.
Loads need to access the cache: The hit time thit is 5ns, the miss time tmiss is 200ns.
The hit rate for loads rhit is 80%.
Application:
app has 1million instructions
20% of instructions are loads.

## Slide 20: Answer on Execution Time
A1: Without considering memory system:
texe,nomem = I * CPI * (1/f_clock) = 1e6 * 1.5 * (1 / 100e6Hz) = 15 ms
t_clock = 1/ f_clock = 10ns
Cache hit time for loads = 5ns < t_clock -> no wait cycles
Cache miss time = 5ns + tmiss = 205ns > t_clock
-> Wait cycles for cache misses cc_stall,miss = roundup((205-10ns)/10ns= 20
-> We have to wait extra 20 cycles for each cache miss for loads
How many loads do we have? 20% of instructions
-> #loads = #Instr * 0,2 = 200 000
How many cache misses do wee have in total?
-> # cache misses = # loads * (1-rhit) = 200000 * (1-0,8) = 40 000
How many extra cycles do we have when we wait for load data and how long do we wait?
-> stall cycles = 40 000 * 20 = 800 000
-> extra waiting time = 800 000 * t_clock = 8 ms
Execution time with memory system:
-> texe= 15ms + 8ms = 23 ms

## Slide 21: Problems on On-chip Buses

## Slide 22: Question on On-Chip Buses
Q1: Given is the following architecture for a shared layered bus:
There are two initiator components, CPU and DMA.
There are three target components, MEM, HWacc and IO. The MEM, is on layer 1, the Hwacc and IO component is on layer 2.
a) Draw the bus architecture. It is sufficient to show the directed connections between components and arbiters/decoders by combining the address and write data bus.
b) Assume that the CPU wants to read access the MEM slave component in the bus cycle 1 and that the DMA wants to read access the HWacc in the same bus cycle 1. Draw the bus access diagram for the data and address bus of the two bus masters as well as the control request and grant signals for the two layers assuming that the bus does not support pipelining. The MEM component inserts no wait cycles. The HWacc component inserts two wait cycles. The arbitration order is this time DMA first, then CPU.

## Slide 23: Answer Layered Bus
ADDR
WDATA
RDATA
HRDATA
MEM
M u x
M u x
M u x
ArbiterLayer1
Decoder1
CPU
ADDR
WDATA
RDATA
M u x
Decoder2
DMA
HRDATA
HWacc
M u x
M u x
ArbiterLayer2
HRDATA
IO
M u x
Decoder
A1:

## Slide 24: Problems on HW/SW Interface

## Slide 25: Questions on the HW/SW Interface
Q1: Given the following definition of the register interface. Write the C-Code to set all bits of the bitfield x1 to 1 without modifying the values in bitfield x2.
Device1
0x50 00 00 00
0x50 00 00 04
0x50 00 00 08
31
0
31
0
31
0
x2
y
z
rw
rw
r
7
x1

## Slide 26: Answers on the HW/SW Interface
struct device1_data {
uint32_t x;
uint32_t y;
uint32_t z;
}
void Hwacc_set_x1()
{
uint32_t x = device1_data_ptr->x;
x = config | 0x000000FF;
Hwacc_data_ptr->x = x;
}
A1: